## Slide 1: Fourier-Wavelet Regularized Deconvolution (ForWaRD)
Seminar: Embedded Image Processing
Supervisor: Yousef Baroud Prof: Simon

## Slide 2: Outline
Results & Conclusion
Forward on GPU
Forward
Deblurring Algorithms
R.Neelamani, SP 2004
J.Dysart, HPEC 2014
Notes: Explain what u gonna cover In brief, Example in forward and in forward on gpu.

## Slide 3: Introduction & Motivation
PSF
Blurred Image
AWGN
Original Image
PSF- Point Spread Function
AWGN - Additive White Gaussian Noise

## Slide 4: Introduction & Motivation
Operator Inversion
  Naive Deconvolution(Inverse fourier trans)
    f (x,y)*g(x,y) + n(x,y) = h(x,y)
  Limitation: Large Mean Square error
How to estimate the original image?
Deblurring Algorithms
Notes: Explain f(x,y) and all terms

## Slide 5: Deblurring Algorithms
Wiener Estimation
  Deblurring in Fourier Domain
FoRWaRD Algorithm
  Deblurring in Fourier & Wavelet Domains

## Slide 6: Wiener Estimation
Wiener Filter
Strength: Colored Noise - Sharp images
Limitation: Singularities - unclear edges
Fourier Transform
Filtering
Inverse Fourier Transform
Image
Image
Ref[3]: Digital Image Processing, C. Gonzalez

## Slide 7: FoRWaRD Idea
Input : Sample image
Step1 : Operator Inversion
Step 2: Fourier Transformations
Step 3: Wavelet Transformations
Output: Estimated Image
Inversion
Fourier
Domain
Wavelet
Domain
Observation
o/p

## Slide 8: Wavelet Domain
HF
LF
2
Level 1 coefficients
Image
Level 2
Level 3
HF - High pass Filter
LF - Low pass Filter
2
Down sampling
2
HF
HF
LF
LF
2
2
2
2

## Slide 9: Wavelet Domain
Ref: https://en.wikipedia.org/wiki/DWT
Notes: Read Wikipedia and get expert knowledge on this picture.
Dabauschies 30 40 …..what the other guy told ? Listen to his audio u took on july 1st , (Important)

## Slide 10: FoRWaRD Algorithm
Fourier Shrinkage -
Wavelet Shrinkage - Coefficients Threshold
Smoothens regions, edges well preserved
Observation
o/p
Inversion
Fourier
Shrinkage
Wavelet
Shrinkage

## Slide 11: FoRWaRD Choices
Fourier shrinkage
  Wiener / Tikhonov filter
Wavelet Shrinkage
    WT1 Daubechies transform(6 levels)
    WT2 Daubechies transform(2 levels)
    Wavelet Domain Wiener Filter(WDWF)
Ref[1]: Fourier wavelet regularized deconvolution
for ill-conditioned systems, R.Neelamani

## Slide 12: FoRWaRD Implementation
WT1
PSF
FFT
Fourier Filter
IFFT
WT2
WT1
Estimate Noise
Blurred Image
Compute Threshold
MAD Noise Estimate
PSF - Point Spread Function
Precompute
Threshold Update
Wavelet Transforms
FFT - Forward Fourier
Transform
IFFT - Inverse FFT
WT1
WT2
MAD - Median Absolute
Deviation

## Slide 13: FoRWaRD Implementation
FFT
Filter in Frequency Domain
IFFT
WT2
WT1
Hard Threshold
IWT1
WT2
WDWF
Deblurring
IWT1 - Inverse WT of WT1
IWT2 - Inverse WT of WT2
WDWF – Wavelet Domain
Wiener Filter

## Slide 14: FoRWaRD Implementation
FFT
WT1
PSF
FFT
Fourier Filter
IFFT
WT2
WT1
Estimate Noise
Blurred Image
Filter in Frequency Domain
IFFT
WT2
WT1
Hard Threshold
IWT1
WT2
WDWF
Deblurred Image
Compute
Threshold
MAD Noise Estimate
IWT2

## Slide 15: Results Comparison
  Ref[8]: http://dsp.rice.edu/software/forward
Notes: Imporant : Mention this is the output u gor from matlab code implementation
If possible, add the other image of 1d signal result too.

## Slide 16: FoRWaRD Implementation on GPU
Goal: Real time HD video deblurring (30 f/s)
2 Algorithms to reach goal
Limitation: Bandwidth
DDGPU library (Demosaic & Deblur on GPU)
  Modify Forward
    Remove WDWF, Subframes for Thresh.
Deblurring
Demosaicing

## Slide 17: FoRWaRD Implementation on GPU
Implement DDGPU
    Gpu cards - GTX 580, GTX 670, GTX 780
Performance Improvements
  Reduced memory transfers
  Reduced unnecessary data movements
Notes: Insert if u have time and understood the table contett presented in this ieee paper , here.

## Slide 18: Forward Implementation Comparison
FoRWaRD | FoRWaRD on GPU
Huge computations | Parallel Computations (Multi core)
High Memory bandwidth | Minimizing bandwidth
Grayscale images | Colored images (1080x1920 24-bit pixel )
Ref[2]: Embedded Real time HD Video Deblurring, J.Dysart
Notes: How memoer bandwidth minimized ? Get clear on this point.

## Slide 19: Conclusion
Deconvolution in any single domain is inadequate
Forward Combines Fourier & wavelet Domains
Forward achieves good visual quality
Code open source
Future: Gpu cards  Fpga’s

## Slide 20: References
[1] R. Neelamani, H. Choi, and R. Baraniuk, ‘Forward: Fourierwavelet regularized deconvolution for ill-conditioned systems
[2] J. Dysart, B. Brockman, S. Johnes, F. Bacon “Embedded Realtime HD Video Deblurring
[3] C. Gonzalez, E.Woods, “Digital Signal Processing,” ,Pearson,
[4] T. Young,J. Gerbrands,J. van Vliet, “Fundamentals of Image
Processing,” Delft University of Technology.
[5] Y. Nievergelt, “Wavelets Made Easy,” Birkhaeuser, 1999.
[6] J. Kalifa and S. Mallat, “Thresholding estimators for linear inverse problems,’Ann. Statist.,’, vol. 31,no. 1, Feb 2003.
[7] S. Mallat, A Wavelet Tour of Signal Processing. New York:
Academic, 1998.
[8] http://dsp.rice.edu/software/forward

## Slide 21
తెలుగు
Telugu