## Slide 1: Fourier-Wavelet Regularized Deconvolution (ForWaRD)
Seminar: Embedded Image Processing
Professor: Simon Supervisor: Yousef Baroud

## Slide 2: Outline
Results & Conclusion
ForWaRD on GPU
ForWaRD
Deblurring Algorithms
R.Neelamani, SP 2004
J.Dysart, HPEC 2014

## Slide 3: Introduction
PSF
Blurred Image
AWGN
Original Image
PSF- Point Spread Function
AWGN - Additive White Gaussian Noise

## Slide 4: Motivation
Image blur Model: f (x,y)*g(x,y) + n(x,y) = h(x,y)
Naive Deconvolution (Inverse fourier transform)
  1/G(w)
  Limitation: Large Mean Square error
How to estimate the original image?
Deblurring Algorithms

## Slide 5: Deblurring Algorithms
Image Deblurring Techniques
Blind Deconvolution
Non Blind Deconvolution
Wiener Filter
Regularized
Filter
ForWaRD
Haar

## Slide 6: Wiener Deconvolution
Wiener Filter
J = deconvwnr(I,PSF,NSR)
Fourier Transform
Filtering
Inverse Fourier Transform
Image
Image
Ref[3]: Digital Image Processing, C. Gonzalez

## Slide 7: Wiener Filter Result
+ Sharp images
- Singularities

## Slide 8: Wavelet Domain
LF
HF
2
Level 1 coefficients
Image
Level 2
Level 3
HF - High pass Filter
LF - Low pass Filter
2
Down sampling
2
LF
LF
HF
HF
2
2
2
2

## Slide 9: Haar Wavelet Transform
Forward Transform
  At each level
    Scaling coefficients
      Avg. of adjacent samples
    Wavelet coefficients
      Sub. of adjacent samples
[ca,ch,cv,cd]=Dwt2(X, ‘wname’)

## Slide 10: Wavelet Transform Result
+ Smooth regions
- Noise

## Slide 11: ForWaRD Algorithm
Fourier Shrinkage
  Tikhonov filter, K= 3.4*10-4
Wavelet Shrinkage
  Coefficients Threshold : Y = wthresh(X,SORH,T)
  Wavelet domain wiener filter
Observation
o/p
Wavelet
Shrinkage
Wavelet Shrinkage
Fourier Shrinkage
Inversion
Ref[1]: R. Neelamani, ‘Forward for ill conditioned systems’

## Slide 12: ForWaRD Implementation
WT1
PSF
FFT
Regularized Fourier Filter
IFFT
WT2
WT1
Estimate Noise
Blurred Image
Compute Threshold
MAD Noise Estimate
PSF - Point Spread Function
Precompute
Threshold Update
Daubechies6, 2
Wavelet Transforms
FFT - Forward Fourier
Transform
IFFT - Inverse FFT
WT1
WT2
MAD - Median Absolute
Deviation

## Slide 13: ForWaRD Implementation
FFT
Filter in Frequency Domain
IFFT
WT2
WT1
Hard Threshold
IWT1
WT2
WDWF
Deblurring
IWT1 - Inverse WT of WT1
WDWF – Wavelet Domain
Wiener Filter
Blurred Image

## Slide 14: ForWaRD Implementation
FFT
WT1
PSF
FFT
Regularized Fourier Filter
IFFT
WT2
WT1
Estimate Noise
Blurred Image
Filter in Frequency Domain
IFFT
WT2
WT1
Hard Threshold
IWT1
WT2
WDWF
Deblurred Image
Compute
Threshold
MAD Noise Estimate
IWT2

## Slide 15: Results Comparison
  Ref[8]: http://dsp.rice.edu/software/forward

## Slide 16: ForWaRD Implementation on GPU
Real time HD video deblurring (30 f/s)
  Camera + Processor + GPU
DDGPU library (Demosaic & Deblur on GPU)
  Reduced ForWaRD
    Remove WDWF, Subframes for Thresholding
Performance Improvements
  Reduced memory transfers
  Reduced unnecessary data movements
Ref[2]: J. Dysart “Embedded Realtime HD Video Deblurring

## Slide 17: ForWaRD Performance Results
Implement DDGPU on GPU cards
Time/frame (ms) | Color | GPU | Improvements
55 | Gray | GTX 580 | Removed device transfers
100 | Color | GTX 580 | Reduced Computations
37.5 | Color | GTX 670 | Full Reduced Algorithm
23 | Color | GTX 780 | Upgraded Hardware

## Slide 18: ForWaRD Implementation Comparison
ForWaRD | ForWaRD on GPU
Huge computations | Parallel Computations (Multi core)
High Memory bandwidth | Minimized bandwidth
Grayscale images | Colored images

## Slide 19: Conclusion
Deconvolution in any single domain is inadequate
Forward combines fourier & wavelet domains
Better Estimate than traditional filters
Improved MSE  Good visual quality
Space variant applications
Future: Gpu cards  Fpga’s
Notes: Code open source
Smoothens regions, edges well preserved
Applications of forward ranges from satellite imaging to seismic deconvolution. Can be used in all Space variant systems

## Slide 20: References
[1] R. Neelamani, H. Choi, and R. Baraniuk, ‘Forward:
Fourierwavelet regularized deconvolution for ill-conditioned
systems
[2] J. Dysart, B. Brockman, S. Johnes, F. Bacon “Embedded
Realtime HD Video Deblurring
[3] C. Gonzalez, E.Woods, “Digital Signal Processing,” ,Pearson,
[4] T. Young,J. Gerbrands,J. van Vliet, “Fundamentals of Image
Processing,” Delft University of Technology.
[5] Y. Nievergelt, “Wavelets Made Easy,” Birkhaeuser, 1999.
[6] J. Kalifa and S. Mallat, “Thresholding estimators for linear
inverse problems,’Ann. Statist.,’, vol. 31,no. 1, Feb 2003.
[7] S. Mallat, A Wavelet Tour of Signal Processing. New York:
Academic, 1998.
[8] http://dsp.rice.edu/software/forward

## Slide 21
DANKE Thank you